Add psram

The ESP32-2432S032C (a 3.2" display variant similar to the "Cheap Yellow Display" family) does not have built-in external PSRAM on most standard versions — your board matches that description (no PSRAM chip soldered, but empty landing pads/footprint visible on the PCB).
These empty pads are typically a SOIC-8 (8-pin narrow) footprint, designed as an optional spot for adding either:
- Extra SPI flash (for more storage)
- Or PSRAM (to add external pseudo-static RAM, usually 4 MB or 8 MB)
This is a common design choice on many cheap ESP32 + TFT boards to keep base cost low while allowing upgrades.
### Compatible Chip to Solder
The footprint is almost always wired in parallel with the existing SPI flash (shared CLK, MOSI, MISO, CS lines + dedicated CE for PSRAM), and the voltage is 3.3 V on this board family (not 1.8 V).
Recommended / most compatible chips (based on ESP32 official support + community successes on similar boards like ESP32-2432S028R / CYD variants):
- ESP-PSRAM32 or ESP-PSRAM32H (Espressif's own 4 MB PSRAM) — safest software compatibility
- ESP-PSRAM64 or ESP-PSRAM64H (8 MB version) — if you want more RAM
- Equivalent third-party clones that work well in practice:
  - LY68L6400 (or IPS6404LSQ / IPS6404L-SQ-SPN) — 8 MB, very popular "drop-in" on these cheap displays
  - APM/SPM series like APM32F103 equivalents aren't PSRAM; stick to the above
Key requirements:
- Package: SOIC-8 (150 mil / narrow body, 1.27 mm pitch) — exactly matches the footprint
- Voltage: 3.3 V operation (your board uses 3.3 V VDD for SPI)
- Interface: Quad SPI (4 data lines) — the pads support it (shared with flash)
- Size: 4 MB (32 Mbit) or 8 MB (64 Mbit) — ESP32 can address up to ~4–16 MB depending on config, but 8 MB is common and stable
### Soldering Steps (High-Level)
1. Identify the footprint — usually near the ESP32 module or flash chip, labeled something like "U2" or "PSRAM" on silkscreen (or just 8 pads in a row).
2. Buy the chip — e.g., search AliExpress / LCSC / DigiKey for "ESP-PSRAM64H SOIC8" or "LY68L6400 SOIC8" (cheap, ~$1–2).
3. Soldering — Use a fine-tip iron or hot air station:
  1. Tin the pads lightly.
  2. Align pin 1 (notch/dot on chip) with pin 1 on PCB (usually marked).
  3. Solder carefully — no bridges (pins are close).
  4. No extra pull-ups/resistors needed on most of these boards (strapping is handled).
4. Software enable (critical — without this, it won't be detected):
  1. In PlatformIO platformio.ini:
    text
    board_build.psram_type = enabled ; or qio / opi if your chip requires it
  2. Or in Arduino IDE: Tools → PSRAM → "Enabled" (or "OPI PSRAM" for some 8 MB chips).
  3. In code: Check with psramFound() or ESP.getPsramSize() — should return >0 after reboot.
  4. For LVGL: It will automatically use PSRAM for larger buffers if enabled → helps your DMA allocation error.
### Warnings / Reality Check
- Success rate: ~70–90% on these boards — many people add LY68L6400 successfully, but some variants have missing traces, wrong voltage, or CS line not broken out → won't work.
- Risk: Bad soldering can short SPI lines → brick the flash → board dead. Use flux, magnifying glass, test continuity first.
- If it doesn't work: The pads might be for flash only (some boards do this) — check with multimeter (probe CLK/MOSI to see if connected to ESP32 pins 6/7/8/11 or similar).
- Alternative: If soldering feels too risky, consider a different ESP32 board with built-in PSRAM (e.g., ESP32-S3 with 8 MB PSRAM is cheap now) or optimize your code to use less RAM (smaller LVGL buffers, no full-screen images).
If you can share a close-up photo of the empty footprint (or the board top/bottom), I can help confirm the exact pinout/wiring. Otherwise, start with ESP-PSRAM64H or LY68L6400 in SOIC-8 — those are the go-to choices for these displays. Good luck with the mod!